Simple Siren
Hackerspace Charlotte
Raspberry Pi Night
November 3, 2016

---
Setup
- Connect Arduino to Raspberry Pi
- Power on Raspberry Pi
- Red light should be ON on the Arduino
- Start Arduino IDE

---
Code Siren Program
#define LED 5 //The pin # of the LED
#define SPEAKER 3 //The pin # of the speaker
#define BUTTON 7 //The pin # of the button
int i = 0; //Used for counting
int val = LOW; //Stores whether the button is pressed or not.
int old_val = LOW; //Stores whether the button was pressed or not last time around the loop.
int state = 0; //The on/off state of our siren.
void setup()
{
  pinMode(LED, OUTPUT); //Tells arduino that the LED is an output
  pinMode(SPEAKER, OUTPUT); //Tells arduino that the speaker is an output
  pinMode(BUTTON, INPUT); //Tells the arduino that the button is an input
    //Fade LED and Speaker on.
    for(i = 0; i < 255; i = i + 2)
    {
      analogWrite(SPEAKER, i);
      delay(10);
    }
    //Fade LED and Speaker out.
    for(i = 255; i > 1; i = i - 2)
    {
      analogWrite(SPEAKER, i);
      delay(10);
    }
    //Flash LED and Speaker on and off.
    for(i = 1; i <= 10; i++)
    {
      analogWrite(SPEAKER, 200);
      delay(100);
      analogWrite(SPEAKER, 25);
      delay(100);
    }
    //Turn of the speaker
    analogWrite(SPEAKER, 0);
}
void loop()
{
}

---
Siren page 1
#define LED 5 //The pin # of the LED
#define SPEAKER 3 //The pin # of the speaker
#define BUTTON 7 //The pin # of the button
int i = 0; //Used for counting

---
Siren page 2
void setup()
{
  pinMode(LED, OUTPUT); //Tells arduino that the LED is an output
  pinMode(SPEAKER, OUTPUT); //Tells arduino that the speaker is an output
  pinMode(BUTTON, INPUT); //Tells the arduino that the button is an input
    //Fade LED and Speaker on.
    for(i = 0; i < 255; i = i + 2

---
Siren page 3
{
      analogWrite(SPEAKER, i);
      delay(10);
    }
    //Fade LED and Speaker out.
    for(i = 255; i > 1; i = i - 2)
    {
      analogWrite(SPEAKER, i);
      delay(10);
    }

---
Siren page 4
//Flash LED and Speaker on and off.
    for(i = 1; i <= 10; i++)
    {
      analogWrite(SPEAKER, 200);
      delay(100);
      analogWrite(SPEAKER, 25);
      delay(100);
    }
    //Turn of the speaker
    analogWrite(SPEAKER, 0);
}

---
Siren page 5
void loop()
{
}

---
Wire Speaker to Arduino
- Black wire to ground
- Red wire to D3

---
Run Siren Program
- Save the Siren program
  - File → Save As
- Upload to the Arduino
  - Sketch → Upload
- Program will only run once since it is inside the setup loop

---
Connect Water Sensor
- Connect ribbon cable to sensor
  - Black = ground
  - Red = 5v
  - Yellow = Analog
- Connect Arduino pins to ribbon cable
  - Black = gnd
  - Red = 5v
  - Yellow = A5

---
Alter Program
- Merge the two programs together
- Use If Else statement to control when siren sounds

---
References
http://www.instructables.com/id/Make-a-Mini-LED-Siren-powered-by-Arduino/